## Slide 1: A Matrix-free Algorithm for Reduced-space PDE-governed Optimization
Pengfei Meng

## Slide 2
Introduction
Homotopy-Based Globalization
Matrix-free Preconditioner
Tests and Applications
Contributions and Recommendations
Outline

## Slide 3
Introduction  Optimization  Preconditioner  Tests  Summary
Improved engineering design is needed to address climate change
Notes: https://www.mercurynews.com/2017/04/24/extreme-weather-linked-to-greenhouse-gases-stanford-study-says/

## Slide 4
Introduction  Optimization  Preconditioner  Tests  Summary
Aviation can reduce its emissions by improving aircraft through optimization

## Slide 5
Optimization problems with state-based constraints are common, yet challenging to solve
Aero-Structural Optimization
Kenway and Martins [16]
Topology Optimization
Kennedy [17]
Introduction  Optimization  Preconditioner  Tests  Summary
Notes: PDE solution is a subproblem associated with optimization, major cost; solving the PDE equation, adjoint equation is the most expensive part;
Size is very large, as the state and adjoint solve size mesh-dependent ; large-scale
discretized Euler equation

## Slide 6
Conventional optimization algorithms are poorly suited for state-based constraints
Conventional (matrix-based) optimization algorithms require the explicit total constraint Jacobian
The gradient of each constraint requires the solution of a linear PDE (the adjoint)
Cost is intractable when there are hundreds of constraints
Storing the (dense) constraint Jacobian can also be expensive
Introduction  Optimization  Preconditioner  Tests  Summary
Notes: Conventional optimization algorithms have been used on PDE-governed optimization problems
When there are relatively few state-based constraints, SNOPT, IPOPT, Knitro

## Slide 7
We will consider the following, generic PDE-constrained optimization problem
Introduction  Optimization  Preconditioner  Tests  Summary
The Lagrangian:
Notes: Be sure to give the audience concrete examples of each of these functions. You can do this using either text or orally.
For example, f can be drag or weight, or range. h might be a lift constraint. g might be stress or bound constraints, etc.
S: is for slack variables ; x, u

## Slide 8
A coupled, nonlinear system of equations
ill-conditioned
potentially large
Optimal designs satisfy the first-order optimality conditions (KKT condition)
State Equation:
Adjoint Equation:
Complementarity:
Introduction  Optimization  Preconditioner  Tests  Summary
Notes: Complementarity e:

## Slide 9
The full-space KKT-system is large (at least 2 times the number of states), indefinite, and ill-conditioned
Globalization algorithms for nonlinear PDEs are difficult to incorporate into full-space methods
If the full-space optimization does not converge, the PDE is not even satisfied and cannot be used to inform decision making
The full-space approach solves all the variables simultaneously, including the PDE state and adjoint
Introduction  Optimization  Preconditioner  Tests  Summary
Notes: In optimization iteration, the state and adjoint solve do not converge tightly.

## Slide 10
The reduced-space approach treats the PDE state and adjoint as implicit functions
Reduced-space methods can make use of existing simulation solvers and adjoint solvers
The reduced-space optimization system is much smaller than the full-space system
Reduced-space algorithms have been successfully applied to unconstrained and equality-constrained problems
Introduction  Optimization  Preconditioner  Tests  Summary

## Slide 11
An advantage of the reduced-space approach is its modular structure
Introduction  Optimization  Preconditioner  Tests  Summary
Mesh Movement
Initial Design, x0
Final Design, x*
Solve PDE
Optimization Algorithm
Converged?
Solve Adjoint(s)
Gradient(s) ?
Yes
Yes
No
No
Notes: Optimality and feasibility

## Slide 12
The reduced-space KKT conditions are as follows:
Introduction  Optimization  Preconditioner  Tests  Summary
Notes: Note that the dependence on the state and adjoint vector has been omitted, as for each new x, state and adjoint are updated implicitly;

## Slide 13
Inexact-Newton methods are attractive for solving the reduced-space problem
This way the explicit Hessian and the explicit total constraint Jacobian are not required
We solve the root-finding problem using a Newton-based approach
The cost of the KKT-vector products is virtually independent of the number of design variables and nonlinear constraints
The KKT-vector products are evaluated matrix-freely using second-order adjoints
Introduction  Optimization  Preconditioner  Tests  Summary

## Slide 14
The following challenges must be addressed in order to use inexact-Newton methods for general nonlinear constraints
Globalization: must avoid stationary points that are not local minimizers, i.e. handle nonconvexity.
Preconditioning: accelerate the convergence of Krylov iterative methods in a matrix-free way.
Introduction  Optimization  Preconditioner  Tests  Summary

## Slide 15
Introduction
Homotopy-Based Globalization
Matrix-free Preconditioner
Tests and Applications
Contributions and Recommendations
Outline

## Slide 16
A homotopy map defines a solution path from an easy-to-obtain solution to the desired solution
Introduction  Optimization  Preconditioner  Tests  Summary
The desired problem:
The easy problem:
Notes: The solution trajectory, the path of x, goes from the zero of the simple function to the zero of the original function;
Each curve represents a solution trajectory for different value of a;
For this simple problem, the method is globally convergent, as different a, or different starting point, all lead to the same solution

## Slide 17
For constrained optimization we use the following convex homotopy
Introduction  Optimization  Preconditioner  Tests  Summary
The Jacobian of the Homotopy function is

## Slide 18
A predictor-corrector algorithm is used to trace the homotopy zero-curve
Introduction  Optimization  Preconditioner  Tests  Summary
In predictor step:
In corrector step:
Notes: It will be easier to describe the algorithm first without mentioning inexact solves.

## Slide 19
In practice, the predictor and corrector steps use inexact solves
Introduction  Optimization  Preconditioner  Tests  Summary
In predictor step:
In corrector step:
Notes: Be sure to explain orally that this grey curve is the zero contour of H, and that it gives the desired solution when \mu= 0.
Methods for tracing the solution curve of the homotopy; one type of predictor-corrector algorithm;
Calculate the tangential direction of the solution curve for updating q and mu; then mu is fixed, Newton-Krylov method to bring the predictor point closer to the solution curve;
go back two slides and explain that this is how the red lines on slide 8 are created.

## Slide 20
The tangent linear problem in the predictor step involves several steps:
1. Inexact Krylov solve:
2. The tangent direction is obtained from
3. The predictor point is calculated as follows:
Introduction  Optimization  Preconditioner  Tests  Summary

## Slide 21
The step-size is controlled adaptively to help keep the predictor close to the zero curve
Introduction  Optimization  Preconditioner  Tests  Summary
Initial parameters:
Step-size factor:
Step-size:

## Slide 22
The slack variables and inequality multipliers must be safeguarded
Slack Variable
Inequality Multipliers
Introduction  Optimization  Preconditioner  Tests  Summary

## Slide 23
Globalization Experiment 1: Sphere Problem
True Solution:
Local Maximizer:
Problem Formulation:
Introduction  Optimization  Preconditioner  Tests  Summary
Notes: At the beginning of the solution path, when mu equals 1, the simple KKT system is at play;
At the end of the solution path, when mu equals 0, the true KKT system is in effect. In the middle, it’s a mixture of the two.
The simple KKT system has nice properties: the reduced Hessian is positive definite, and the calculated design update would be a feasible descent direction.
The added homotopy term functions as regularization and globalization unit;
When the true KKT system has nonconvex Hessian, the added regularization from the simple KKT helps the trajectory enter the neighborhood of the local minimum for the original problem; help bypass the local maximum stationery point;
Newton method behave poorly around stationery point, indefinite matrix

## Slide 24
Introduction  Optimization  Preconditioner  Tests  Summary
Globalization Experiment 1: Sphere Problem
The initial guesses were generated by adding Gaussian perturbations, , to each coordinate of

## Slide 25
Introduction  Optimization  Preconditioner  Tests  Summary
Globalization Experiment 1: Sphere Problem
As a second test, the initial guesses were generated by standard normal distribution around the origin

## Slide 26
Globalization Experiment 2: Non-convex Problem
-1
1
0
Qi = 1
-1
1
0
Qi = -1
The pattern of the Hessian matrix and the initial point
are both randomly generated
Problem Formulation:
Introduction  Optimization  Preconditioner  Tests  Summary

## Slide 27
Introduction  Optimization  Preconditioner  Tests  Summary
Globalization Experiment 2: Non-convex Problem

## Slide 28
Introduction  Optimization  Preconditioner  Tests  Summary
Globalization Experiment 2: Non-convex Problem
The optimization criteria are described later

## Slide 29
Introduction
Homotopy-Based Globalization
Matrix-free Preconditioner
Tests and Applications
Contributions and Recommendations
Outline

## Slide 30
The most expensive part of the matrix-free algorithm is inexactly solving the linear systems
Predictor Step
Newton Step in Corrector
Introduction  Optimization  Preconditioner  Tests  Summary
The linear systems that arise are solved inexactly using Flexible GMRES
Notes: Mention orally that you will describe the approach to solving these linear systems in the next section of the presentation.

## Slide 31
The true KKT system in optimization is ill-conditioned, FGMRES will stall without an effective preconditioner.
A preconditioner transforms the linear system to a better conditioned one with the same solution:
General preconditioners based on an explicit matrix are not applicable, e.g. ILU factorizations.
The reduced-space KKT system must be preconditioned
Introduction  Optimization  Preconditioner  Tests  Summary

## Slide 32
The preconditioner is trying to approximately solve the following system

## Slide 33
For inequality-only constrained problems, the matrix-free preconditioner involves three steps
Step 1: elimination of the slack and multiplier terms
using the Schur complement
Introduction  Optimization  Preconditioner  Tests  Summary
Notes: Be sure to explain orally the challenges associated with inverting C_\mu.

## Slide 34
Step 2: Use a Lanczos SVD approximation for the constraint Jacobian terms
Step 3: Apply the Sherman-Morrison formula to obtain the desired design update
Introduction  Optimization  Preconditioner  Tests  Summary
For inequality-only constrained problems, the matrix-free preconditioner involves three steps
Notes: Be sure to explain orally that the Lanczos method only requires matrix-vector product, and that these matrix-vector products are approximated inexpensively by using the PDE preconditioner in place of a full PDE solve.
Orally, explain what A and UV are in the context of the above matrices.

## Slide 35
When equality constraints are included, the Schur complement is augmented
To solve this, is kept away from zero in the preconditioner using the clipping rule ; consequently, the system can be solved approximated as follows.
Introduction  Optimization  Preconditioner  Tests  Summary
The Lanczos SVD approximation is applied to the sum of the equality and inequality Jacobian terms
Notes: This way, the augmented Schur complement is calculated matrix-freely, and the slack and inequality multipliers can be retrieved as before.

## Slide 36
The algorithms have been implemented in a Python library[44]
Algorithms have been implemented in Kona, a matrix-free optimization package for PDE-constrained problems
Kona uses the following convergence metrics:
For benchmarking, we compare against SNOPT, which is a state-of-the-art active-set algorithm frequently used in the engineering optimization community
Introduction  Optimization  Preconditioner  Tests  Summary

## Slide 37
Preconditioner Experiment: Scalable Quadratic Problem
Randomly generated orthonormal matrix
Introduction  Optimization  Preconditioner  Tests  Summary
Problem Formulation:
The singular values of and are predefined:
Notes: Dimension of the problem n : 100, 200, 300, 400, 500
Q and A are full rank matrices, condition number unchanged when dimension increases
condition number unchanged when dimension increases
be sure to explain why you are considering this problem.

## Slide 38
This simple example illustrates the effectiveness of the preconditioner
Introduction  Optimization  Preconditioner  Tests  Summary
200 design variables

## Slide 39
Introduction  Optimization  Preconditioner  Tests  Summary
500 design variables
This simple example illustrates the effectiveness of the preconditioner

## Slide 40
The proposed preconditioner helps the inexact-Newton algorithm scale well with problem size; second
Introduction  Optimization  Preconditioner  Tests  Summary
(seconds)

## Slide 41
Introduction
Homotopy-Based Globalization
Iterative Solver & Preconditioner
Tests and Applications
Contributions and Recommendations
Outline

## Slide 42
The algorithms were verified on a subset of the CUTEr test suite, a collection of test problems for optimization algorithms
Introduction  Optimization  Preconditioner  Tests  Summary
A summary of Table 4.1, which contains the test results of a subset of the CUTEr problems:
Overall 63 problems are tested
Kona accurate: 60
SNOPT accurate: 39
The following types of problems are excluded:
Notes: What cuter is??

## Slide 43
PDE-governed problem 1: Stress-Constrained Mass Minimization
Introduction  Optimization  Preconditioner  Tests  Summary
The governing PDE models the response of the plate to the applied force using linear elasticity with 2D plane stress
Notes: X: thickness of each element
F: structural constitutive equation between thickness distribution x and displacements

## Slide 44
The preconditioner is required to ensure convergence of the Krylov iterative method
Introduction  Optimization  Preconditioner  Tests  Summary
Krylov-solver convergence history corresponding to the first Newton for the first Newton step at the final corrector phase for the small case

## Slide 45
The proposed algorithm is able to converge the problem on all three grids
Small
Introduction  Optimization  Preconditioner  Tests  Summary

## Slide 46
Medium
Introduction  Optimization  Preconditioner  Tests  Summary
The proposed algorithm is able to converge the problem on all three grids
Notes: SVD preconditioner is effective helping with convergence
The increasing cost with scaling is driven by increasing SVD ranks
SNOPT has difficulty locating active constraints

## Slide 47
Large
Introduction  Optimization  Preconditioner  Tests  Summary
The proposed algorithm is able to converge the problem on all three grids

## Slide 48
The thickness distribution obtained using the three methods is slightly different
New method with preconditioner
New method without preconditioner
SNOPT

## Slide 49
PDE-governed problem 2: Aerodynamic Shape Optimization Problem
Introduction  Optimization  Preconditioner  Tests  Summary
NASA Common Research Model (CRM) wing defined by AIAA/ADODG

## Slide 50
Free-form deformation is used to parameterize the wing shape [ Adflow / FFD ]
Introduction  Optimization  Preconditioner  Tests  Summary
Three different sized FFD control volumes were considered

## Slide 51
Aerodynamic coefficient history and optimization plots from Kona
Introduction  Optimization  Preconditioner  Tests  Summary
Number of Design: 768

## Slide 52
Introduction  Optimization  Preconditioner  Tests  Summary
Aerodynamic coefficient history and optimization plots from SNOPT
Number of Design: 768

## Slide 53
Introduction
Homotopy-Based Globalization
Iterative Solver & Preconditioner
Tests and Applications
Contributions and Recommendations
Outline

## Slide 54
Contributions
Developed a reduced-space Newton-Krylov method for general constrained PDE-governed design problems
Used a Homotopy-based method to increase the reduced-space inexact-Newton method’s globalization capacity
Created a novel and effective matrix-free preconditioner to accelerate the convergence rate of the iterative methods
Introduction  Optimization  Preconditioner  Tests  Summary

## Slide 55
Introduction  Optimization  Preconditioner  Tests  Summary
No "silver bullet" preconditioner: provide preconditioners for different types of problems in Kona
Separate the nonlinear and linear constraints in Kona’s API
Improve the robustness of the method in the context of non-convex problems
Improve the efficiency of the preconditioner for ASO problem and run the RANS-based optimization
Investigate methods to automate the parameter values
Recommendations

## Slide 56
Thank you!
Questions?

## Slide 57
Backup Slide

## Slide 58
The optimization package Kona:
is a matrix-free optimization package designed to solve reduced-space PDE-constrained problems
separates the optimization algorithms from PDE-solver specific implementations
has a solver interface that provides Jacobian-vector and vector-Jacobian products that are necessary to assemble total sensitivities
Introduction  Optimization  Preconditioner  Tests  Summary